→ on_button_pressed(0)

→ on_button_pressed(1)

→ on_button_pressed(2)

→ on_button_pressed(3)
← display_show(line #, text)
→ on_drawer_filled(0)
→ on_drawer_dropped(0)
← drawer_drop_can(0)
→ on_drawer_filled(1)
→ on_drawer_dropped(1)
← drawer_drop_can(1)
→ on_cash_inserted(200)
→ on_cash_inserted(100)
→ on_cash_inserted(50)
→ on_cash_filled(200)
→ on_cash_filled(100)
→ on_cash_filled(50)
← cash_drop_coin(200)
← cash_drop_coin(100)
← cash_drop_coin(50)
→ on_bin_fetch_all
→ on_bin_entry

Handout

Embedded Vending Machine

Agile Engineering Course

# Overview
Vending machine is a piece of hardware containing sensors and actuators for its components.
- Sensors register events from hardware components in the machine
  Sensors are therefore input for the software and output for the hardware. The control software can subscribe to events from specific sensors.
- Actuators pass information to the hardware components
  Actuators are therefore output for the software and input for the hardware.

sensor

SOFTWARE
HARDWARE

actuator

# Development
## Ruby Code organization
lib/	controller code
test/	tests for controller code
features/	story tests and steps
To deploy your controller code to the simulator, execute rake deploy
To run your tests, execute rake (or autotest to run them automatically).
To run the story tests, execute rake features
## C# Code organization
The solution consists of 5 projects:
Project	Description
VendingMachine.Controller	Contains the control software that you need to write. / The Adapter directory contains the sensor collection and the actuator collection that control should use to respond to sensor events and initiate actuator events
VendingMachine.Controller.unittests	Unit tests for the control software.
VendingMachine.Controller.specs	Feature tests for the control software
VendingMachine.Simulator	Contains hardware components simulating the hardware (directory Hardware) and the simulator GUI. This is also the startup project.
VendingMachine.Simulator.unittests	Unit tests for the hardware components

## Where's the main?
Ruby:
Your objects controlling the machine are loaded by the executable lib/main.rb. An example:

require "vmlog"
require 'devices'

module Control
  include VMLog

  def self.main
    # here, you should load your vending machine control software

# as an example of using the actuators and sensors (seedoc/actuators_and_sensors)
    Devices.display_show(0, 'Choose')
    Devices.display_show(1, 'Please...')

    Devices.on_button_pressed(0) do
      log "cola pressed"

      Devices.display_show(0, 'Cola')
    end
  end
end

You can use the log function from the VMLog module to print message to stderr.
C#:
Your starting point for the control software is the VendingMachineController class, which has an OnLoad method that is called on startup:
public class VendingMachineController
{
    public void OnLoad()
    {
      // here, your vending machine control software will be loaded
    }
}
## Subscribe to a sensor event
Ruby:
      Devices.on_button_pressed(1) do
   # put your event handling code here
end

C#:
SensorCollection.Instance().On(":button_press_0", delegate() {
        this.ButtonPressed();
      });
## Fire an actuator
Ruby:
      Devices.display_show(1, "test message")

      Devices.drawer_drop_can(1)

C#:
ActuatorCollection.Instance().Fire(":drawer_drop_can_3");

ActuatorCollection.Instance().Fire(":display_show",
new Object[] {0, "credits: 0"});
# Hardware components
## Buttons
Buttons register presses and contain sensors to notify software. The system contains the following buttons:
button_no	description
0	The cola button
1	The fanta button
2	The sprite button
3	The sisi button

### Sensors
on_button_press(<button_no>)
fires when a button is pressed
<button_no> is the number of the button
## Drawers
Drawers contains cans of beverage. Drawers can drop cans into the bin. They contain actuators to drop a can and sensors to detect that a can is added to the drawer (fill) and to detect that a can has been dropped (drop). The system contains the following drawers:
drawer_no	description
0	The cola drawer
1	The fanta drawer
2	The sprite drawer
3	The sisi drawer

### Sensors
- on_drawer_drop_can(<drawer_no>)
  fires on dropping a can
  <drawer_no> is the number of the drawer
- on_drawer_fill_can(<drawer_no>)
  fires on putting a new can in the drawer
  <drawer_no> is the number of the drawer
### Actuators
drawer_drop_can(<drawer_no>)
tells a drawer to drop a can
<drawer_no> is the number of the drawer

## Display
The display can show messages to the user. It contains two lines. The system has only one display.
### Actuators
display_show (<line_no>, <message>)
tells the display to show a message
<line_no> is the number of the line (0 based)
<message> is the message to display
## Cash register
The cash register can accept coins and drop them into the bin (to give money back). The cash register contains actuators to drop different types of coins and sensors to notify that a coin is inserted into the cash register. It recognizes the following coins:
coin_type	description
50	50 cents
100	1 euro
200	2 euro

### Sensors
- on_cash_fill(<coin_type>)
  fires on filling a coin in the cash register's stock
  <coin_type> is the type of coin added
- on_cash_insert(<coin_type>)
  fires on inserting a coin in the cash register as a paying action
  <coin_type> is the type of coin added
### Actuators
cash_drop(<coin_type>)
tells cash_register to drop a coin in the bin as a change return action
<coin_type> is the type of coin to drop (50, 100, 200)
## Bin
The bin catches cans and change. It contain sensors to detect cans or coins entering the bin and to detect that the bin is emptied,
### Sensors
- on_bin_entry
  fires on something (a coin or a can) falling in the bin
- on_bin_fetch_all
  fires on something (a coin or a can) fetched from the bin by a user.